Gravity compensation
System architecture:
Input: Master system's current arm configuration (joint positions)
Output: joint torque

Parameter Identification:
Replicate the parameter identification process from the previous project using the least square method to determine the unknown parameters based on data collection of torques and joint configurations.

Forward Kinematics:
The forward kinematics of the arm is acquired from direct measurement of the physical system. We use the home configuration to determine the position for forward kinematics.

block diagram:

Code:
- The gravity compensation algorithm is created using the Newton-Euler approach with velocity and acceleration set to 0. In the code, the we have the forward kinematics schematic for arm configuration determination which requires current joint positions. Currently, we hard-coded the velocity and acceleration in order to satisfy the condition of this project.
- The robot parameters have already been determined in the previous project. However, we still need to understand how they were acquired.
- In the previous work, the algorithm was done in MATLAB. To keep things simple and easy for ROS communication, we use Python for this project instead.

Process:
- The system provides several parameters needed for the gravity compensation code. First, we requires the master system current joint configuration for torque computation. For the gravity compensation, the joint velocity and acceleration must remain in static state (must be 0).

ROS:
the joint_state topic (contains current joint position, velocity, and effort) is published at 20 Hz rate.

NewtonEuler code tests:
Effort comparison at home configuration (joint_states msgs): MTMR
Actual:
~[-0.10888387297460854, 0.620031200730383, 0.620031200730383, 0.3130967381247525, 0.09083351051637077, -0.017922679598429924, 0.0012691958322377077, 2.638487576630867e-05]
Computed:
[ 0. -0.59645835 -0.59645835 0.20413122 0.14498558 0.11782822 6.71161253 -7.6311755 ]
Effort comparison at home configuration (joint_states msgs): MTML
Actual:
[-0.04690332005754798, 0.530493819414924, 0.530493819414924, 0.21566561119888567, -0.0740242035872299, -0.02424935336259663, 0.001989282512344319, 1.566421787502076e-05]
Computed:
[ 0. -0.59728953 -0.59728953 0.19501315 0.15256946 0.17895355 6.72406565 -7.57800548]

** The torque is way off.

Using the old MATLAB code: the computed torque is not quite accurate (a little bit higher than actual torque). The parameters and regressor matrices must be re-identified.
Since MATLAB can now be run on Ubuntu, the process of connection between ROS and MATLAB is significantly simplified and more convenient than when the RBE501 team ran it on laptop.

**Caution: Do not manually apply torque to joints. It might break the robot.